## Slide 1: GPU Computing with opencl
FRANCISCO PAULO DE ABOIM

## Slide 2: PUC-Rio
Francisco Paulo de Aboim
  Graduated in Civil Engineering in 2009 with emphasis in Structures at PUC-Rio
  Second year of Msc in Civil Engineering at PUC-Rio
  Thesis: Finite Element Solver in OpenCL
  Researcher at TecGraf in the Sigma3D modeling project
Notes: PUC and tecgraf intro

## Slide 3: What is OpenCL?
Standard defined by a consortium of industry leaders (AMD, Intel, Apple, Nvidia, IBM…)
Heterogeneous programming platform, meaning not only GPUs but also CPUs, DSP, Accelerators (i.e. IBM CELL)
Exposes underlying memory architecture implying more control and, therefore, potential performance gains
Notes: CELL-BE, intel 80 processor research project, llhano APU

## Slide 4: Pros/Cons of Porting Code to OpenCL
Takes longer to program code and (much longer) to debug
Incipient technology – risk of not becoming well established
Code is harder to maintain
Because of the above development and maintenance costs are higher
Harder than most of what normal human beings use
Much larger potential throughput per $ spent
Better energy efficiency – Eco friendly and cheaper to run
Exposes underlying memory architecture implying more control and, therefore, potential performance gains
Code can port to different heterogeneous platforms
Easier than IL
Pros
Cons
Notes: Cypress low-level GPU architecture

## Slide 5: Moore’s law and GPUs
Processor transistor count doubles every two years
Clock speeds remain pretty much the same!
Instructions per clock also hit a wall (0,5 inst./clock)
Solution: more cores packed into one processor!
Because of the above development and maintenance costs are higher
“CPU scaling predicted by Moore’s Law is now dead” – Nvidia VP
AMD GPUs
Moore’s Law (CPUs)
Notes: Moore’s Law, Memory wall, Clock wall, Instruction Wall

## Slide 6: Moore’s law and GPUs
Processor transistor count doubles every two years
Clock speeds remain pretty much the same!
Instructions per clock also hit a wall (0,5 inst./clock)
Solution: more cores packed into one processor!
Because of the above development and maintenance costs are higher
“CPU scaling predicted by Moore’s Law is now dead” – Nvidia VP
AMD GPUs
Moore’s Law (CPUs)
Notes: Cypress low-level GPU architecture

## Slide 7: The power consumption problem
22nm gate is about 74 silicon atoms wide
Leakage is becoming an issue – quantum tunneling
Limits processor’s speeds and presents cooling problem

## Slide 8: “Current” Hardware
Peak Performance

## Slide 9: How did we get here?
Highly competitive gaming industry
Process more pixels and triangles - faster
Advent of (progammable) shaders
GLSL GPU computing “hack”
Recently the need for realtime video filters and image processing also fit well into the GPU model and has been adopted by the industry
Notes: What lead to current GPU performance

## Slide 10: AMD GPU Hardware Architecture
AMD 5870 ( Cypress Core ):
20 SIMD engines
16 SIMD units per core
5 multiply-adds per functional unit (VLIW processing)
2.72 Teraflops Single Precision
544 Gigaflops Double Precision
Source: Introductory OpenCL SAAHPC2010, Benedict R. Gaster
Notes: Cypress low-level GPU architecture

## Slide 11: SIMD Engine
A SIMD engine consists of a set of “Stream Cores”
Stream cores arranged as a five way Very Long Instruction Word (VLIW) processor
  Up to five scalar operations can be issued in a VLIW instruction
  Scalar operations executed on each processing element
Stream cores within compute unit execute same VLIW instruction
  The block of work-items that are executed together is called a wavefront.
  64 work items for 5870
One SIMD Engine
General Purpose Registers
One Stream Core
T-Processing
Element
Branch
Execution Unit
Processing
Elements
Instruction and Control Flow
Notes: SIMD engine discussion

## Slide 12: SIMD Engine
A SIMD engine consists of a set of “Stream Cores”
Stream cores arranged as a five way Very Long Instruction Word (VLIW) processor
  Up to five scalar operations can be issued in a VLIW instruction
  Scalar operations executed on each processing element
Stream cores within compute unit execute same VLIW instruction
  The block of work-items that are executed together is called a wavefront.
  64 work items for 5870
Source: AMD Accelerated Parallel Processing OpenCL Programming Guide
Notes: SIMD engine discussion

## Slide 13: What??????
Traditional Von Neumann Architecture
  Instructions are in memory
  Data is also in the same memory
  ALU is the “calculator”
  Most basic model
Source: Wikipedia
Notes: SIMD engine discussion

## Slide 14: Modified Harvard Architecture
There are basically a fixed number of instructions
Separate memory for instructions – can be read only.
Data and instructions can be loaded simultaneously
Source: Wikipedia
Notes: Von Neumann Evolution and the modified harvard architecture

## Slide 15: Vector Processor Architecture
SIMD – Single Instruction Multiple Data
Data parallelism(SIMD) x Task Parallelism(SPMD)
Same instruction operating on a vector of data
Program executes in lockstep
SSE and MMX for the x86 architecture
CELL BE – one scalar and eight vector processors
Source: Wikipedia
Notes: History of vector processors

## Slide 16: SIMT Execution Model
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
…
Wavefront
…
Cycle
SIMD Width
SIMD execution can be combined with pipelining.
  ALUs all execute the same instruction
  Pipelining is used to break instruction into phases
  When first instruction completes (4 cycles here), the next instruction is ready to execute
Latency
hiding
Notes: The SIMT Execution mode which shows how different threads execute the same instruction

## Slide 17: Cache Memory
While clock speeds have increased memory speeds have increased very little in the last 20 years.
Faster memory is possible but it costs much more
With the intel 386 chip, cache was introduced as an off chip add-on
Since the 486 has become standardized on chip and has included more levels as time progressed
Source: tomshardware.com
Notes: Memory caches and the advent of hierarchical memory

## Slide 18: Cache Memory
While clock speeds have increased memory speeds have increased very little in the last 20 years.
Faster memory is possible but it costs much more
With the intel 386 chip, cache was introduced as an off chip add-on
Since the 486 has become standardized on chip and has included more levels as time progressed
Source: tomshardware.com
Notes: Memory caches and the advent of hierarchical memory

## Slide 19: Cache Memory
While clock speeds have increased memory speeds have increased very little in the last 20 years.
Faster memory is possible but it costs much more
With the intel 386 chip, cache was introduced as an off chip add-on
Since the 486 has become standardized on chip and has included more levels as time progressed
Source: tomshardware.com
Notes: Memory caches and the advent of hierarchical memory

## Slide 20: Cache Memory
While clock speeds have increased memory speeds have increased very little in the last 20 years.
Faster memory is possible but it costs much more
With the intel 386 chip, cache was introduced as an off chip add-on
Since the 486 has become standardized on chip and has included more levels as time progressed
Solution to the memory bound problem – memory hierarchies
Source: tomshardware.com
Notes: Memory caches and the advent of hierarchical memory

## Slide 21: AMD Memory Model in OpenCL
Subset of hardware memory exposed in OpenCL
Local Data Share (LDS) exposed as local memory
  Share data between items of a work group designed to increase performance
  High Bandwidth access per SIMD Engine
Private memory utilizes registers per work item
Constant Memory
  __constant tags utilize L1 cache.
Global Memory
Private
Memory
Workitem 1
Private
Memory
Workitem 1
Compute Unit 1
Local Memory
Global / Constant Memory Data Cache
Local Memory
Private
Memory
Workitem 1
Private
Memory
Workitem 1
Compute Unit N
Compute Device
Compute Device Memory
Notes: The mapping of the AMD GPU memory components to the OpenCL terminology.
Architecturally this is similar for AMD and Nvidia except that each ones have their own vendor specific names
Similar types of memory are mapped to local memory for both AMD and Nvidia

## Slide 22: Back to the stream core..
A SIMD engine consists of a set of “Stream Cores”
Stream cores arranged as a five way Very Long Instruction Word (VLIW) processor
  Up to five scalar operations can be issued in a VLIW instruction
  Scalar operations executed on each processing element
General Purpose Registers
One Stream Core
Special
Function
Unit
Control
Flow
ALU Units
Instruction and Control Flow
Source: AMD Accelerated Parallel Processing OpenCL Programming Guide
Notes: Return to discussion of the stream core

## Slide 23: Back to the stream core..
Source: AMD Accelerated Parallel Processing OpenCL Programming Guide
General Purpose Registers
One Stream Core
Special
Function
Unit
Control
Flow
ALU Units
Instruction and Control Flow
One Double Precision Unit
One Double Precision Unit
A SIMD engine consists of a set of “Stream Cores”
Stream cores arranged as a five way Very Long Instruction Word (VLIW) processor
  Up to five scalar operations can be issued in a VLIW instruction
  Scalar operations executed on each processing element
Notes: Return to discussion of the stream core

## Slide 24: Back to the stream core..
A SIMD engine consists of a set of “Stream Cores”
Stream cores arranged as a five way Very Long Instruction Word (VLIW) processor
  Up to five scalar operations can be issued in a VLIW instruction
  Scalar operations executed on each processing element
All stream cores within compute unit execute same VLIW instruction
  The block of work-items that are executed together is called a wavefront.
  64 work items for 5870
Source: AMD Accelerated Parallel Processing OpenCL Programming Guide
Notes: Return to discussion of the stream core

## Slide 25: Big Picture

## Slide 26: AMD Platform as seen in OpenCL
Individual work-items execute on a single processing element
Processing element refers to a single VLIW core
Multiple work-groups execute on a compute unit
A compute unit refers to a SIMD Engine
Notes: We converge back to the OpenCL terminology to understand how the AMD GPU maps onto the OpenCL processing elements

## Slide 27: An Optimal GPGPU Kernel
From the discussion on hardware we see that an ideal kernel for a GPU:
  Has thousands of independent pieces of work
    Uses all available compute units
    Allows interleaving for latency hiding
  Is amenable to instruction stream sharing
    Maps to SIMD execution by preventing divergence between work items
  Has high arithmetic intensity
    Ratio of math operations to memory access is high
    Not limited by memory bandwidth
Note that these caveats apply to all GPUs
Notes: Discusses an optimal kernel to show how irrespective of the different underlying architecture, an optimum program for both AMD and Nvidia would have similar characteristics

## Slide 28: OpenCL Compilation System
LLVM - Low Level Virtual Machine
Kernels compiled to LLVM IR
Open Source Compiler
  Platform, OS independent
  Multiple back ends
http://llvm.org
OpenCL Compute Program
LLVM IR
Nvidia PTX
AMD CAL IL
x86
LLVM Front-end
Notes: Explains how platform agnostic OpenCL code is mapped to a device specific Instruction Set Architecture.

## Slide 29: Thread Structure
Massively parallel programs are usually written so that each thread computes one part of a problem
  For vector addition, we will add corresponding elements from two arrays, so each thread will perform one addition
  If we think about the thread structure visually, the threads will usually be arranged in the same shape as the data

## Slide 30: Thread Structure
More work items the better for latency hiding
Threads within the OpenCL framework are called “work items”
Work items are arranged into workgroups which can share data within local memory
Barrier can be implemented for threads within a workgroup

## Slide 31: Thread Structure
Work-items can uniquely identify themselves based on:
  A global id (unique within the index space)
  A work-group ID and a local ID within the work-group

## Slide 32: Example Kernel
Simple vector addition kernel:
__kernel
void vecadd(__global int* A,
__global int* B,
__global int* C) {
int tid = get_global_id(0);
C[tid] = A[tid] + B[tid];
}

## Slide 33: Thread Structure
Consider a simple vector addition of 16 elements
  2 input buffers (A, B) and 1 output buffer (C) are required
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A
B
C
=
+
Vector Addition:
Array Indices

## Slide 34: Thread Structure
Create thread structure to match the problem
  1-dimensional problem in this case
Thread structure:
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A
B
C
=
+
Vector Addition:
14
15
12
13
10
11
8
9
6
7
4
5
2
3
0
1
Thread IDs

## Slide 35: Thread Structure
Each thread is responsible for adding the indices corresponding to its ID
Thread structure:
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A
B
C
=
+
Vector Addition:
14
15
12
13
10
11
8
9
6
7
4
5
2
3
0
1

## Slide 36: Take Away
Great for problems with large numbers of parallel threads and high computational intensity (e.g. Matrix Multiplication)
For full utilization of the hardware it’s necessary to find a way to fully utilize the different levels of the memory hierarchy
Branching is GPU computing’s nemesis!
Workgroup size tuning is not deterministic and takes time and lots of trial and error

## Slide 37: Thanks, see you in Rio!